## Slide 1: Computer Organization and Design Performance
Montek Singh
Jan 13, 2016
Lecture 2

## Slide 2: Topics
Defining “Performance”
Performance Measures
How to improve performance
Performance pitfalls
Examples

## Slide 3: Why Study Performance?
Helps us make intelligent design choices
  See through the marketing hype
Key to understanding underlying computer organization
  Why is some hardware faster than others for different programs?
  What factors of system performance are hardware related?
    e.g., Do we need a new machine …
    … or a new operating system?
  How does a machine’s instruction set affect its performance?

## Slide 4: What is Performance?
Loosely:
  How fast can a computer complete a task
Examples of “tasks”:
  Short tasks:
    Crunch a bunch of numbers (say calculate mean)
    Display a PDF document
    Respond to a game console button press
  Longer ones:
    Search for a document on hard drive
    Rip a CD track into an mp3 file
    Apply a Photoshop filter
    Transcode/recode a video

## Slide 5: Which airplane is “best”?
Airplane
Passenger capacity
Cruising range (miles)
Cruising speed (mph)
Passenger throughput (passengers x mph)
Chart: 
| Douglas DC-8-50 | BAC/Sud Concorde | Boeing 747 | Boeing 777
Passenger Capacity | 146 | 132 | 470 | 375
Chart: 
| Douglas DC-8-50 | BAC/Sud Concorde | Boeing 747 | Boeing 777
Cruising Range (miles) | 8720 | 4000 | 4150 | 4630
Chart: 
| Douglas DC-8-50 | BAC/Sud Concorde | Boeing 747 | Boeing 777
Cruising Speed (mph) | 544 | 1350 | 610 | 610

## Slide 6: Which airplane is “best”?
How much faster is the Concorde than the 747?
  2.2 X (“X” means “factor of”)
How much larger is the 747’s capacity than the Concorde?
  3.6 X
It is roughly 4000 miles from Raleigh to Paris. What is the throughput of the 747 in passengers/hr? The Concorde?
What is the latency (trip time) of the 747? The Concorde?
  6.56 hours, 2.96 hours
Airplane
Passenger capacity
Cruising range (miles)
Cruising speed (mph)
Passenger throughput (passengers x mph)

## Slide 7: Performance Metrics
Latency: Time from input to corresponding output
  How long does it take for my program to run?
  How long must I wait after typing return for the result?
  Other examples?
Throughput: Results produced per unit time
  How many results can be processed per second?
  What is the average execution rate of my program?
  How much work is getting done each second?
  Other examples?

## Slide 8: Design Tradeoffs
Performance is rarely the sole factor
  Cost is important too
  Energy/power consumption is often critical
Frequently used compound metrics
  Performance/Cost (throughput/$)
  Performance/Power (throughput/watt)
  Work/Energy (total work done per joule)
    for battery-powered devices

## Slide 9: Execution Time
Elapsed Time/Wall Clock Time
  counts everything (disk and memory accesses, I/O, etc.)
  includes the impact of other programs
  a useful number, but often not good for comparison purposes
CPU time
  does not include I/O or time spent running other programs
  can be broken up into system time, and user time
Our focus: user CPU time
  time spent executing actual instructions of “our” program

## Slide 10: Performance
For some program running on machine X,
  PerformanceX = Program Executions / TimeX (executions/sec)
  = 1 / Execution TimeX
Relative Performance
  "X is n times faster than Y”
  PerformanceX / PerformanceY = n
Example:
  Machine A runs a program in 20 seconds
  Machine B runs the same program in 25 seconds
    By how much is A faster than B?
    By how much is B slower than A?
PerformanceA = 1/20
PerformanceB = 1/25
Machine A is (1/20)/(1/25) = 1.25 times faster than Machine B

## Slide 11: Performance: Pitfalls of using %
Same Example:
  Machine A runs a program in 20 sec; B takes 25 sec
  By how much is A faster than B?
    Is it (25-20)/25 = 20% faster?
    Is it (25-20)/20 = 25% faster?
    Correct answer is: A is (PerfA-PerfB)/PerB faster
      (0.05 - 0.04) / (0.04) = 25% faster
  By how much is B slower than A?
    Correct answer is: B is (PerfB-PerfA)/PerA faster/slower
      (0.04 - 0.05) / (0.05) = -20% faster = 20% slower
  Confusing: A is 25% faster than B; B is 20% slower
  Better: A is 1.25 times faster than B; B is 1/1.25 as fast
Also: %ages are only good up to 100%
  Never say A is 13000% faster than B

## Slide 12: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 1/(0.25ns) = 4GHz = 4000MHz = 4.0×109Hz
Clock (cycles)
Data transfer and computation
Update state
Clock period

## Slide 13: Program Clock Cycles
Instead of reporting execution time in seconds, we often use clock cycle counts
  Why? A newer generation of the same processor…
    Often has the same cycle counts for the same program
    But often has different clock speed (ex, 1 GHz changes to 1.5 GHz)
Clock “ticks” indicate when machine state changes
  an abstraction: allows time to be discrete instead of continuous
Simple relation:
time

## Slide 14: Program Clock Cycles
Relation:
  or:
  cycle time = time between ticks = seconds per cycle
  clock rate (frequency) = cycles per second (1 Hz = 1 cycle/s)
  A 200 MHz clock has a cycle time of:

## Slide 15: Instruction Count and CPI
Instruction Count for a program
  Determined by
    program
    Instruction set architecture (ISA)
    compiler
Average cycles per instruction (“CPI”)
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 16: Computer Performance Measure
Millions of Instructions per Second
Frequency in MHz
Historically:
PDP-11, VAX, Intel 8086: CPI > 1
  Load/Store RISC machines MIPS, SPARC, PowerPC, miniMIPS: CPI = 1
  Modern CPUs, Pentium, Athlon : CPI < 1
CPI (Average Clocks Per Instruction)
Unfortunate coincidence:
This “MIPS” has nothing to do with the name of the MIPS processor we will be studying!

## Slide 17: How to Improve Performance?
Many ways to write the same equations:
So, to improve performance (everything else being equal) you can either
  ________ the # of required cycles for a program;
  ________ the clock cycle time or, said another way,
  ________ the clock rate;
  ________ the CPI (average clocks per instruction).
MIPS Pitfall
  Cannot compare MIPS of two different processors if they run different sets of instructions!
   Meaningless Indicator of Processor Speed!
Decrease
Decrease
Increase
Decrease

## Slide 18: How Many Cycles in a Program?
For some processors (e.g., MIPS processor)
  # of cycles = # of instructions
This assumption can be incorrect, Different instructions take different amounts of time on different machines.
Memory accesses might require more cycles than other instructions.
Floating-Point instructions might require multiple clock cycles to execute.
Branches might stall execution rate
time
1st instruction
2nd instruction
3rd instruction
4th
5th
6th
...
Notes: Each instruction can generally be done in one clock cycle in a MIPS processor, but not always

## Slide 19: Example
Our favorite program runs in 10 seconds on computer A, which has a 2 GHz clock. We are trying to help a computer designer build a new machine B, to run this program in 6 seconds. The designer can use new (or perhaps more expensive) technology to substantially increase the clock rate, but has informed us that this increase will affect the rest of the CPU design, causing machine B to require 1.2 times as many clock cycles as machine A for the same program. What clock rate should we tell the designer to target?

## Slide 20: Now that we understand cycles
A given program will require
  some number of instructions (machine instructions)
  some number of cycles
  some number of seconds
We have a vocabulary that relates these quantities:
  cycle time (seconds per cycle)
  clock rate (cycles per second)
  CPI (average clocks per instruction)
    a floating point intensive application might have a higher CPI
  MIPS (millions of instructions per second)
    this would be higher for a program using simple instructions

## Slide 21: Performance Traps
Performance is determined by the execution time of a program that you care about.
Do any of the other variables equal performance?
  # of cycles to execute program?
  # of instructions in program?
  # of cycles per second?
  average # of cycles per instruction?
  average # of instructions per second?
Common pitfall:
  Thinking that only one of the variables is indicative of performance when it really is not!

## Slide 22: CPI Example
Suppose we have two implementations of the same instruction set architecture (ISA)
  If two machines have the same ISA which quantity (e.g., clock rate, CPI) is the same?
  For some program:
    Computer A has a clock cycle time of 250 ps and a CPI of 2.0
    Computer B has a clock cycle time of 500 ps and a CPI of 1.2
  What machine is faster for this program, and by how much?
A is faster by 1.2 X

## Slide 23: CPI in More Detail
If different instruction classes take different numbers of cycles
  Weighted average CPI:
Relative frequency

## Slide 24: Example: Compiler’s Impact
Two different compilers are being tested for a 500 MHz machine with three different classes of instructions: Class A, Class B, and Class C, which require one, two, and three cycles (respectively). Both compilers are used to produce code for a large piece of software. The first compiler's code uses 5 million Class A instructions, 1 million Class B instructions, and 2 million Class C instructions. The second compiler's code uses 7 million Class A instructions, 1 million Class B instructions, and 1 million Class C instructions.
Which program uses fewer instructions?
  Instructions1 = (5+1+2) x 106 = 8 x 106
  Instructions2 = (7+1+1) x 106 = 9 x 106
Which sequence uses fewer clock cycles?
  Cycles1 = (5(1)+1(2)+2(3)) x 106 = 13 x 106
  Cycles2 = (7(1)+1(2)+1(3)) x 106 = 12 x 106
CPI1 = ?
13/8 = 1.625
CPI2 = ?
12/9 = 1.33

## Slide 25: CPI Example
Alternative compiled code versions using instructions in classes A, B, C
Version 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Class | A | B | C
CPI for class | 1 | 2 | 3
IC for version 1 | 2 | 1 | 2
IC for version 2 | 4 | 1 | 1
Version 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 26: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Cycle Time
The BIG Picture

## Slide 27: Benchmarks
Performance best determined by running a real application
  Use programs typical of expected workload
  Or, typical of expected class of applications
    e.g., compilers/editors, scientific applications, graphics, etc.
Small benchmarks
  nice for architects and designers
  easy to standardize
  can be abused
SPEC (System Performance Evaluation Cooperative)
  companies have agreed on a set of real program and inputs
  can still be abused
  valuable indicator of performance (and compiler technology)

## Slide 28: SPEC ’95
Periodically updated with newer benchmarks
  SPEC 2000, SPEC 2006

## Slide 29: SPEC 2006
Interesting to see how the mix of applications has changed over the years…
  See http://www.spec.org/cpu2006/{CINT2006, CFP2006}

## Slide 30: Other Popular Benchmarks
Several others popular
  industry uses SPEC
  but ordinary consumers use others
    more representative of the work they do!
      e.g., gaming, Photoshop/Aperture, copying huge files, multimedia coding/decoding, etc.
    Geekbench is quite popular!

## Slide 31: Amdahl’s Law
Possibly the most important law regarding computer performance:
  Principle: Make the common case fast!
  Eventually, performance gains will be limited by what cannot be improved
    e.g., you can raise the highway speed limit, but the city speed limit stays the same

## Slide 32: Amdahl’s Law: Example
Example: "Suppose a program runs in 100 seconds on a machine, where multiplies are executed 80% of the time. How much do we need to improve the speed of multiplication if we want the program to run 4 times faster?" How about making it 5 times faster?
25 = 80/r + 20 r = 16x
20 = 80/r + 20 r = ?

## Slide 33: Example
Suppose we enhance a machine making all floating-point instructions run FIVE times faster. If the execution time of some benchmark before the floating-point enhancement is 10 seconds, what will the speedup be if only half of the 10 seconds is spent executing floating-point instructions?
We are looking for a benchmark to show off the new floating-point unit described above, and want the overall benchmark to show at least a speedup of 3. What percentage of the execution time would floating-point instructions have to account for in this program in order to yield our desired speedup on this benchmark?
5/5 + 5 = 6 Relative Perf = 10/6 = 1.67 x
100/3 = f/5 + (100 – f) = 100 – 4f/5 f = 83.33

## Slide 34: Power Trends
In CMOS IC technology
×1000
×30
5V → 1V

## Slide 35: Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We cannot reduce voltage further
  We cannot remove more heat
How else can we improve performance?

## Slide 36: Moore’s Law: Uniprocessor Perf.
Constrained by power, instruction-level parallelism, memory latency

## Slide 37: Multiprocessors
“Multicore” microprocessors
  More than one processor core per chip
Requires explicitly parallel programming
  Hardware executes multiple instructions at once
    Ideally, hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization
    But, newer OSes and libraries have been designed for this

## Slide 38: Manufacturing ICs
IC = Integrated Circuit (“chip”)
Yield: proportion of working dies per wafer

## Slide 39: Integrated Circuit Cost
Nonlinear relation to area and defect rate
  Wafer cost and area are fixed
  Defect rate determined by manufacturing process
  Die area determined by architecture and circuit design

## Slide 40: Fallacy: Low Power at Idle
AMD X4 power benchmark:
  At 100% load: 295W (max power)
  At 50% load: 246W (83% max power)
  At 10% load: 180W (still consumes 61% of max power)
Google data center
  Mostly operates at 10% - 50% load
  At 100% load less than 1% of the time
Industry challenge: Design processors to make power proportional to load

## Slide 41: Remember
Performance is specific to a particular program
  Total execution time is a consistent summary of performance
For a given architecture performance comes from:
  increases in clock rate (without adverse CPI affects)
  improvements in processor organization that lower CPI
  compiler enhancements that lower CPI and/or instruction count
Pitfall: Expecting improvements in one aspect of a machine’s performance to affect the total performance
You should not always believe everything you read!
  Read carefully! Especially what the business guys say!

## Slide 42: Concluding Remarks
Cost/performance is improving
  Due to underlying technology development
Hierarchical layers of abstraction
  In both hardware and software
Instruction set architecture
  The hardware/software interface
Execution time: the best performance measure
Power is a limiting factor
  Use parallelism to improve performance