## Slide 1: Computer Organization and Design Instruction Sets - 1
Montek Singh
Feb 1-3, 2016
Lecture 4

## Slide 2: Representing Instructions
Today’s topics
  von Neumann model of a computer
  Instruction set architecture
  MIPS instruction formats
  Some MIPS instructions
Reading
  P&H textbook Ch. 2.1-2.2, Ch. 2.5-2.6

## Slide 3: A General-Purpose Computer
The von Neumann Model
  Many architectural models for a general-purpose computer have been explored
  Most of today’s computers based on the model proposed by John von Neumann in the late 1940s
  Its major components are:
Central
Processing Unit
Central Processing Unit (CPU): Fetches, interprets, and executes a specified set of operations called Instructions.
Main
Memory
Memory: storage of N words of W bits each, where W is a fixed architectural parameter, and N can be expanded to meet needs.
Input/
Output
I/O: Devices for communicating with the outside world.

## Slide 4: Instructions and Programs
What are instructions?
  the words of a computer’s language
Instruction Set
  the full vocabulary
Stored Program Concept
  The idea that instructions and data of many types can be stored in memory as numbers, leading to the stored program computer
    Distinct from “application-specific” hardware, which is “hardwired” to perform “fixed-function” processing on inputs
    Distinct from punched tape computers (e.g., looms) where instructions were not stored, but streamed in one at a time

## Slide 5: Anatomy of an Instruction
An instruction is a primitive operation
  Instructions specify an operation and its operands (the necessary variables to perform the operation)
  Types of operands: immediate, source, and destination
add $t0, $t1, $t2
addi $t0, $t1, 1
Operation
Operands (variables, arguments, etc.)
Source Operands
Destination Operand
Immediate Operand
$X is a convention to denote the contents of a “register”, which is a location inside the CPU. In contrast, immediate operands indicate the value itself

## Slide 6: Meaning of an Instruction
Operations are abbreviated into opcodes (1-4 letters)
Instructions are specified with a very regular syntax
  First an opcode followed by arguments
  Usually (but not always) the destination is next, then source
  Why this order? Arbitrary…
    … but analogous to high-level language like Java or C
add $t0, $t1, $t2
int t0, t1, t2
t0 = t1 + t2
implies
The instruction syntax provides operands in the same order as you would expect in a statement from a high level language.

## Slide 7: Being the Machine!
Instruction sequence
  Instructions are executed sequentially from a list …
    … unless some special instructions alter this flow
  Instructions execute one after another
    therefore, results of all previous instructions have been computed
$t0: 0
$t1: 6
$t2: 8
$t3: 10
Variables
add $t0, $t1, $t1
add $t0, $t0, $t0
add $t0, $t0, $t0
sub $t1, $t0, $t1
Instructions
12
24
48
42
What is this program doing?
Notes: A program is just a definite set of intructions
One line at a time
Read from top to bottom, on the right you have variable values
The first instruction, adds two t1’s and stores them into t0…. T1 is 6 so t0 becomes 12

## Slide 8: What did this machine do?
Let’s repeat the simulation, this time using unknowns
  CLASS: What is this machine doing?
Knowing what the program does allows us to write down its specification, and give it a meaningful name
$t0: w
$t1: x
$t2: y
$t3: z
Variables
add $t0, $t1, $t1
add $t0, $t0, $t0
add $t0, $t0, $t0
sub $t1, $t0, $t1
Instructions
2x
4x
8x
7x
times7:

## Slide 9: Looping the Flow
Need something to change the instruction flow
  “go back” to the beginning
  a jump instruction with opcode ‘j’
    the operand refers to a label of some other instruction
    for now, this is a text label you assign to an instruction
    in reality, the text label becomes a numerical address
$t0: w
$t1: x
$t2: y
$t3: z
Variables
add $t0, $t1, $t1
add $t0, $t0, $t0
add $t0, $t0, $t0
sub $t1, $t0, $t1
Instructions
8x
7x
times7:
j times7
56x
49x
392x
343x
An infinite loop

## Slide 10: Open Questions in our Simple Model
We will answer the following questions next
  WHERE are INSTRUCTIONS stored?
  HOW are instructions represented?
  WHERE are VARIABLES stored?
  How are labels associated with particular instructions?
  How do you access more complicated variable types:
    Arrays?
    Structures?
    Objects?
  Where does a program start executing?
  How does it stop?

## Slide 11: The Stored-Program Computer
The von Neumann model:
  Instructions and Data stored in a common memory (“main memory”)
  Sequential semantics: All instructions execute sequentially (or at least appear sequential to the programmer)
Key idea: Memory holds not only data, but coded instructions that make up a program.
Central
Processing Unit
Main Memory
instruction
instruction
instruction
data
data
data
CPU fetches and executes instructions from memory ...
  The CPU is a hardware interpreter
  Program IS simply data for this interpreter
  Main memory: Single expandable resource pool - constrains both data and program size - don’t need to make separate decisions of how large of a program or data memory to buy
Notes: Any program done in machine language is one instruction at a time

## Slide 12: Anatomy of a von Neumann Computer
Control Unit
Data
Path
registers
MEMORY
control
status
instructions
data
PC
1101000111011
• INSTRUCTIONS coded in binary
• PROGRAM COUNTER or PC: Address of next instruction to be executed
• Control Unit has circuitry inside to translate instructions into control signals for data path
+1
R1 R2+R3
address
address
“Register File”
Register 0
Register 1
Register 31

## Slide 13: Instruction Set Architecture (ISA)
Definition:
  The part of the computer architecture related to programming, including the native data types, instructions, registers, addressing modes, memory architecture, interrupt and exception handling, and external I/O
  An ISA includes a specification of the set of opcodes (machine language), and the native commands implemented by a particular processor

## Slide 14: Instruction Set Architecture (ISA)
Encoding of instructions raises interesting choices...
  Tradeoffs: performance, compactness, programmability
  Complexity
    How many different instructions? What level operations?
      Level of support for particular software operations: array indexing, procedure calls, “polynomial evaluate”, etc.
    “Reduced Instruction Set Computer” (RISC) philosophy: simple instructions, optimized for speed
  Uniformity
    Should different instructions be same size?
    Take the same amount of time to execute?
    Trend favors uniformity  simplicity, speed, cost/power
Mix of Engineering & Art...
  Trial (by simulation) is our best technique for making choices!
Our representative example: the MIPS architecture!

## Slide 15: The big picture
A few things to note:
  Memory is distinct from data path
  Registers are in data path
  Program is stored in memory
  Control unit fetches instructions from memory
  Control unit tells data path what to do
  Data can be moved from memory to registers, or from registers to memory
  All data processing (e.g., arithmetic) takes place within the data path
Control Unit
Data
Path
registers
MEMORY
control
status
instructions
data
address
address

## Slide 16: MIPS Programming Model a representative simple RISC machine
Processor State (inside the CPU)
Main Memory
Fetch/Execute loop:
fetch Mem[PC]
PC = PC + 4†
execute fetched instruction (may change PC!)
repeat!
†MIPS uses byte memory addresses. However, each instruction is 32-bits wide, and *must* be aligned on a multiple of 4 (word) address. Each word contains four 8-bit bytes. Addresses of consecutive instructions (words) differ by 4.
00
PC
r0
r1
r2
...
r31
000000....0
32 bit “words”
0
1
2
3
(4 bytes)
32 bit “words”
0
31
next instruction
General Registers:
A small scratchpad of frequently used or temporary variables
In Comp 411 we’ll use a clean and sufficient subset of the
MIPS-32 core Instruction set.
0 4
8
16 20
Addresses
Notes: 32 bits only can be stored inside each registar
In main memory, first row is address 0 and there are 4 bytes inside of it. With address 0, 1, 2 ,3
Next row has addresses of

## Slide 17: Some MIPS Memory Nits
Memory locations are 32 bits wide
  BUT, they are addressable in different-sized chunks
  8-bit chunks (bytes)
  16-bit chunks (shorts)
  32-bit chunks (words)
  64-bit chunks (longs/double)
We also frequently need access to individual bits! (Instructions help w/ this)
Every BYTE has a unique address (MIPS is a byte-addressable machine)
Every instruction is one word
0
1
2
3
4
5
6
7
Addr
0:
4:
8:
12:
8
9
10
12
12
13
14
15
byte3 byte2 byte1 byte0
short2 short0
long0
long8
31 30 29 … … 4 3 2 1 0
Notes: Bytes can go everywhere.
Shorts can go in either 0&1 or 3&2.

## Slide 18: MIPS Register Nits
There are 32 named registers [$0, $1, …. $31]
The operands of all ALU instructions are registers
  This means to operate on a variables in memory you must:
    Load the value/values from memory into a register
    Perform the instruction
    Store the result back into memory
  Going to and from memory can be expensive
    (4x to 20x slower than operating on a register)
  Net effect: Keep variables in registers as much as possible!
Special purpose and conventions
  2 registers have specific “side-effects”
    (ex: $0 always contains the value ‘0’… more later)
  4 registers dedicated to specific tasks by convention
  26 available for general use, but constrained by convention

## Slide 19: MIPS Instruction Formats
All MIPS instructions fit into a single 32-bit word
Every instruction includes various “fields”:
  a 6-bit operation or “OPCODE”
    specifies which operation to execute (fewer than 64)
  up to three 5-bit OPERAND fields
    each specifies a register (one of 32) as source/destination
  embedded constants
    also called “literals” or “immediates”
    16-bits, 5-bits or 26-bits long
    sometimes treated as signed values, sometimes unsigned
There are three basic instruction formats:
R-type, 3 register operands (2 sources, destination)
I-type, 2 register operands, 16-bit constant
OP
rs
rt
rd
OP
rs
rt
16-bit constant
func
shamt
J-type, no register operands, 26-bit constant
OP
26-bit constant
Notes: 64 different operations because there are 6 bits, aka 2^6 different operations.

## Slide 20: MIPS ALU Operations
Sample coded operation: ADD instruction
What we prefer to write: add $10, $11, $9 (“assembly language”)
add rd, rs, rt:
“Add the contents of rs to the contents of rt; store the result in rd”
Reg[rd] = Reg[rs] + Reg[rt]
arithmetic: add, sub, addu, subu
compare: slt, sltu
logical: and, or, xor, nor
shift: sll, srl, sra, sllv, srav, srlv
Similar instructions for other ALU operations:
0
0
0
0
0
0
0
1
0
1
1
0
1
0
0
1
0
1
0
1
0
1
0
0
0
0
0
0
0
0
0
0
op = 0x00 dictating an ALU function
rs = 11 Reg[11]
source
rd = 10 Reg[10]
destination
rt = 9 Reg[9]
source
unused fields are set to ‘0’
func = 0x20 dictating an add
References to register contents are prefixed by a “$” to distinguish them from constants or memory addresses
R-type:
The convention with MIPS assembly language is to specify the destination operand first, followed by source operands.
Notes: Register 10 gets the value register 11 + register 9
At the binary level, 11 and 9 get added first

## Slide 21: Shift operations
Shifting is a common operation
  applied to groups of bits
  used for alignment
  used for “short cut” arithmetic operations
    X << 1 is often the same as 2*X
    X >> 1 can be the same as X/2
For example:
  X = 2010 = 000101002
  Left Shift:
    (X << 1) = 001010002 = 4010
  Right Shift:
    (X >> 1) = 000010102 = 1010
  Signed or “Arithmetic” Right Shift:
    (-X >>> 1) = (111011002 >>> 1) = 111101102 = -1010

## Slide 22: MIPS Shift Operations
Sample coded operation: SLLV (SLL Variable)
0
0
0
0
0
0
0
0
1
0
0
0
0
0
1
0
0
0
0
1
0
0
0
0
1
0
0
0
0
0
0
0
op = 0x00 dictating an ALU function
shift
amount
in rs
rd = 2 Reg[2]
destination
rt = 2 Reg[2]
source
unused set to ‘0’
func = 0x04 dictating an sllv
Assembly: sllv $2, $2, $8
sllv rd, rt, rs:
“Shift the contents of rt left by the contents of rs; store the result in rd”
Reg[rd] = Reg[rt] << Reg[rs]
This is peculiar syntax for MIPS, in this ALU instruction the rt operand precedes the rs operand. Usually, it’s the other way around
R-type:
Different flavor:
Shift amount is not in instruction, but in a register

## Slide 23: MIPS ALU Operations with Immediate
addi instruction: adds register contents, signed-constant:
Symbolic version: addi $9, $11, -3
“Add the contents of rs to const; store result in rt”
OP = 0x08, dictating addi
rs = 11, Reg[11] source
rt = 9, Reg[9] destination
Reg[rt] = Reg[rs] + sxt(imm)
arithmetic: addi, addiu
compare: slti, sltiu
logical: andi, ori, xori, lui
Similar instructions for other ALU operations:
constant field, indicating -3 as second operand
(sign-extended!)
addi rt, rs, imm:
0
0
1
0
0
0
0
1
0
1
1
0
1
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
Immediate values are sign-extended for arithmetic and compare operations, but not for logical operations.
I-type:

## Slide 24: Why Built-in Constants? (Immediate)
Where are constants/immediates useful?
  SMALL constants used frequently (50% of operands)
    In a C compiler (gcc) 52% of ALU operations use a constant
    In a circuit simulator (spice) 69% involve constants
    e.g., B = B + 1; C = W & 0x00ff; A = B + 0;
Examples: addi $29, $29, 4 slti $8, $18, 10 andi $29, $29, 6 ori $29, $29, 4

## Slide 25: First MIPS Program (fragment)
Suppose you want to compute the expression:
  f = (g + h) – (i + j)
    where variables f, g, h, i, and j are assigned to registers $16, $17, $18, $19, and $20 respectively
    what is the MIPS assembly code?
  Questions to answer:
    How did these variables come to reside in registers?
    Answer: We need more instructions which allow data to be explicitly loaded from memory to registers, and stored from registers to memory
  add $8,$17,$18 # (g + h)
  add $9,$19,$20 # (i + j)
  sub $16,$8,$9 # f = (g + h) – (i + j)

## Slide 26: MIPS Register Usage Conventions
Some MIPS registers assigned to specific uses
  by convention, so programmers can combine code pieces
    will cover the convention later
  $0 is hard-wired to the value 0

## Slide 27: Continue next lecture…
More instructions
  accessing memory
  branches and jumps
  larger constants
  multiply, divide
  etc.