## Slide 1: Computer Organization and Design Instruction Sets - 2
Montek Singh
Feb 10-12, 2016
Lecture 5

## Slide 2: Today
More MIPS instructions
  signed vs. unsigned instructions
  larger constants
  accessing memory
  branches and jumps
  multiply, divide
  comparisons
  logical instructions
Reading
  Book Chapter 2.1-2.7
  Study the inside green flap (“Green Card”)

## Slide 3: Recap: MIPS Instruction Formats
All MIPS instructions fit into a single 32-bit word
Every instruction includes various “fields”:
  a 6-bit operation or “OPCODE”
    specifies which operation to execute (fewer than 64)
  up to three 5-bit OPERAND fields
    each specifies a register (one of 32) as source/destination
  embedded constants
    also called “literals” or “immediates”
    16-bits, 5-bits or 26-bits long
    sometimes treated as signed values, sometimes unsigned
There are three basic instruction formats:
R-type, 3 register operands (2 sources, destination)
I-type, 2 register operands, 16-bit constant
OP
rs
rt
rd
OP
rs
rt
16-bit constant
func
shamt
J-type, no register operands, 26-bit constant
OP
26-bit constant

## Slide 4: Working with Constants
Immediate instructions allow constants to be specified within the instruction
  Examples
    add 2000 to register $5
    addi $5, $5, 2000
    subtract 60 from register $5
    addi $5, $5, -60
      … no subi instruction!
    logically AND $5 with 0x8723 and put the result in $7
    andi $7, $5, 0x8723
    put the number 1234 in $10
    addi $10, $0, 1234
  But…
    these constants are limited to 16 bits only!
      Range is [-32768…32767] if signed, or [0…65535] if unsigned
Notes: No subtract instruction for constants, only add instructions… To subtract 60 you add -60
However, you need a subtraction between variables, because they are variable
All of the numbers are constants of i type, so you have op, rs, rt, and then the 16 bit constant. With these types of instructions you are limmited to 16 bits.

## Slide 5: Recap: ADDI
addi instruction: adds register contents, signed-constant:
Symbolic version: addi $9, $11, -3
“Add the contents of rs to const; store result in rt”
OP = 0x08, dictating addi
rs = 11, Reg[11] source
rt = 9, Reg[9] destination
Reg[rt] = Reg[rs] + sxt(imm)
constant field, indicating -3 as second operand
(sign-extended!)
addi rt, rs, imm:
0
0
1
0
0
0
0
1
0
1
1
0
1
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
I-type:
sign extention pads the sign to make the imm into a 32-bit signed number:
11111111111111111111111111111101
Notes: Value of registar 11 us a 32 bit number, but the constant is only 16
In order to add a 16 bit value to a 32 bit value you need to pad the 16 bit value to make it a 32 bit value (sign extension)
Meaning is take the original value, pad it to the left, add it to the value of Registar rs and store it in the value of registar rt

## Slide 6: ADDIU: Signed vs. Unsigned Constants
addiu instruction: adds register to unsigned-constant:
Symbolic version: addiu $9, $11, 65533
“Add the contents of rs to const; store result in rt”
OP = 0x09, dictating addiu
rs = 11, Reg[11] source
rt = 9, Reg[9] destination
Reg[rt] = Reg[rs] + (imm)
Also: All logical operations are always “unsigned”, so always zero-extended
constant field, indicating 65533 as second operand
(zero-extended!)
addiu rt, rs, imm:
0
0
1
0
0
1
0
1
0
1
1
0
1
0
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
1
I-type:
The imm is 0-padded into a 32-bit unsigned (+ve) number:
00000000000000001111111111111101
Notes: Ad immediate unisnged.
Since there is no sign and everything is positive you just pad with 0’s
Takes the value, pads 0, adds it to Reg rs and stores it in Reg rt.
The u after addi tells the computer that everything is positive
Say it is 0 padded or 0 extended

## Slide 7: How About Larger Constants?
Problem: How do we work with bigger constants?
  Example: Put the 32-bit value 0x5678ABCD in $5
  CLASS: How will you do it?
One Solution:
  put the upper half (0x5678) into $5
  then shift it left by 16 positions (0x5678 0000)
  now “add” the lower half to it (0x5678 0000 + 0xABCD)
  addi $5, $0, 0x5678
  sll $5, $5, 16
  addi $5, $5, 0xABCD
One minor problem with this:
  addi can mess up by treating the constants are signed
  use addiu or ori instead
Notes: The bigger 32 bit value, how do you take the 32 bit constant inside the instruction? No instructions can do this, because all instructions themselves are 32 bit, no instructions can carry the entire number together.
You need to break the number up
Take the upper half and lower half and deal with them separately. Each half is 16 bits
The three lines about:
You are adding 0 to 5678 into registrar 5, meaning that 5678 is in the registrar, meaning it becomes 5678 0000 in hex
Now you move registrar 5 over by 16 bits
Add the other half of the constant ABCD in the lower half of the number
The small problem is addi, sign extends and then adds to registrar 5.
For exqmple A is 1010 so sign extends adds a lot of extra 1’s to the beginning. Brings extra baggage.
Using addiu you can help the ABCD slide in without changing anything else

## Slide 8: How About Larger Constants?
Observation: This sequence is very common!
  so, a special instruction was introduced to make it shorter
  the first two (addi + sll) combo is performed by
  lui
  “load upper immediate”
    puts the 16-bit immediate into the upper half of a register
  Example: Put the 32-bit value 0x5678ABCD in $5
  lui $5, 0x5678
  ori $5, $5, 0xABCD
Notes: Since this is common lui is created so you don’t have to shift.
You use lui to load the upper, and makes the upper half with all 0’s
So when you or it with the lower half it slides in

## Slide 9: How About Larger Constants?
Look at this in more detail:
  “load upper immediate” lui $5, 0x5678 // 0101 0110 0111 1000 in binary
Then must get the lower order bits right
  ori $5, $5, 0xABCD // 1010 1011 1100 1101
0101011001111000
0000000000000000
0000000000000000
1010101111001101
0101011001111000
1010101111001101
ori
0101011001111000
0000000000000000
Reminder: In MIPS, Logical Immediate instructions (ANDI, ORI, XORI) do not sign-extend their constant operand
Notes: Ori, with ABCD does a bit-wise or so if something is 0 if you ori it with something it stays the same.

## Slide 10: Accessing Memory
MIPS is a “load-store” architecture
  all operands for ALU instructions are in registers or immediate
  cannot directly add values residing in memory
    must first bring values into registers from memory (called LOAD)
    must store result of computation back into memory (called STORE)
Control Unit
Data
Path
registers
MEMORY
control
status
instructions
data
address
address
Notes: All arithimitic is done in the data path

## Slide 11: MIPS Load Instruction
Load instruction is I-type
  Does the following:
    takes the value stored in register $rs
    adds to it the immediate value (signed)
    this is the address where memory is looked up
    value found at this address in memory is brought in and stored in register $rt
lw rt, imm(rs)
Meaning: Reg[rt]= Mem[Reg[rs] + sign-ext(imm)]
Abbreviation: lw rt,imm for lw rt, imm($0)
OP
rs
rt
16-bit signed constant
I-type:
Notes: Has an rt and rs registrar with its own op quote
Take the value in registrar rs, takes the immediate in the right half of the expression sign extends it, gives you an address in memory where the actually value is
Puts it in register rt
Suppose rs has the value 100
If immediate has the value 24
Says look at registar rs to which adds the value of the intermediate). Goes to the memory (location 124) reads it gets the value and puts it in value rt

## Slide 12: MIPS Store Instruction
Store instruction is also I-type
  Does the following:
    takes the value stored in register $rs
    adds to it the immediate value (signed)
    this is the address where memory is accessed
    reads the value from register $rt and writes it into the memory at the address computed
sw rt, imm(rs)
Meaning: Mem[Reg[rs] + sign-ext(imm)] = Reg[rt]
Abbreviation: sw rt,imm for sw rt, imm($0)
OP
rs
rt
16-bit signed constant
I-type:

## Slide 13: MIPS Memory Addresses
lw and sw read whole 32-bit words
  so, addresses computed must be multiples of 4
    Reg[rs] + sign-ext(imm) must end in “00” in binary
  otherwise: runtime exception
There are also byte-sized flavors of these instructions
  lb (load byte)
  sb (store byte)
    work the same way, but their addresses do not have to be multiples of 4

## Slide 14: Storage Conventions
Data stored in memory
  addresses in memory are assigned at compile time
  data values must be “loaded” into registers first
  operations done on registers
  result stored in memory
Example
  assume compiler has assigned these memory addresses
1000:
1004:
1008:
1010:
100C:
n
r
x
y
int x, y;
y = x + 37;
lw $t0, 0x1008($0)
addiu $t0, $t0, 37
sw $t0, 0x100C($0)
translates
to:
Compilation approach:
LOAD, COMPUTE, STORE
choice of $t0 is arbitrary

## Slide 15: MIPS Branch Instructions
if (REG[RS] != REG[RT])
{ PC = PC + 4 + 4*offset; }
bne rs, rt, label # Branch if not equal
if (REG[RS] == REG[RT])
{ PC = PC + 4 + 4*offset; }
beq rs, rt, label # Branch if equal
NB: Branch targets are specified relative to the next instruction (which would be fetched by default). The assembler hides the calculation of these offset values from the user, by allowing them to specify a target address (usually a label) and it does the job of computing the offset’s value. The size of the constant field (16-bits) limits the range of branches.
OPCODE
rs
rt
16-bit signed constant
MIPS branch instructions provide a way of conditionally changing the PC to some nearby location...
I-type:
Notice on memory references offsets are multiplied by 4, so that branch targets are restricted to word boundaries.

## Slide 16: MIPS Jumps
The range of MIPS branch instructions is limited to approximately  32K instructions ( 128K bytes) from the branch instruction.
To branch farther: an unconditional jump instruction is used.
Instructions:
  j label # jump to label (PC = PC[31-28] << 28 || CONST[25:0]*4)
  lower 28 bits are the const * 4
  upper 4 bits are from the current PC value
  jal label # jump to label and store PC+4 in $31
  jr $t0 # jump to address specified by register’s contents
  jalr $t0, $ra # jump to address specified by first register’s contents and store PC+4 in second register
Formats:
J-type: used for j
OP = 2
26-bit constant
J-type: used for jal
OP = 3
26-bit constant
R-type, used for jr
OP = 0
rs
func = 8
0
0
0
R-type, used for jalr
OP = 0
rs
func = 9
0
0
rd

## Slide 17: Multiply and Divide
Slightly more complicated than add/subtract
  multiply: product is twice as long!
    if A, B are 32-bit long, A * B is how many bits?
  divide: dividing integer A by B gives two results!
    quotient and remainder
Solution: two new special-purpose registers
  “Hi” and “Lo”

## Slide 18: Multiply
MULT instruction
  mult rs, rt
  Meaning: multiply contents of registers $rs and $rt, and store the (64-bit result) in the pair of special registers {hi, lo}
    hi:lo = $rs * $rt
  upper 32 bits go into hi, lower 32 bits go into lo
To access result, use two new instructions
  mfhi: move from hi
    mfhi rd
      move the 32-bit half result from hi to $rd
  mflo: move from lo
    mflo rd
      move the 32-bit half result from lo to $rd

## Slide 19: Divide
DIV instruction
  div rs, rt
  Meaning: divide contents of register $rs by $rt, and store the quotient in lo, and remainder in hi
    lo = $rs / $rt
    hi = $rs % $rt
To access result, use mfhi and mflo
NOTE: There are also unsigned versions
  multu
  divu

## Slide 20: Now we can do a real program: Factorial...
n: .word 123
ans: .word 0
...
addi $t0, $0, 1 # t0 = 1
lw $t1, n($0) # t1 = n
loop: beq $t1, $0, done # while (t1 != 0)
mult $t0, $t1 # hi:lo = t0 * t1
mflo $t0 # t0 = t0 * t1
addi $t1, $t1, -1 # t1 = t1 - 1
j loop # Always loop back
done: sw $t0, ans($0) # ans = r1
int n, ans, r1, r2;
r1 = 1;
r2 = n;
while (r2 != 0) {
r1 = r1 * r2;
r2 = r2 – 1; }
ans = r1;
Synopsis (in C):
  Input in n, output in ans
  r1, r2 used for temporaries
  assume n is small
MIPS code, in assembly language:
Notes: Done goes to done, if t1 is 0 then it goes to instruction done
If not it will multiply t0 and t1

## Slide 21: Comparison: slt, slti
slt = set-if-less-than
  slt rd, rs, rt
  $rd = ($rs < $rt) // “1” if true and “0” if false
slti = set-if-less-than-immediate
  slt rt, rs, imm
  $rt = ($rs < sign-ext(imm))
also unsigned flavors
  sltu
  sltiu

## Slide 22: Logical Instructions
Boolean operations: bitwise on all 32 bits
  AND, OR, NOR, XOR
  and, andi
  or, ori
  nor // Note: There is no nori
  xor, xori
Examples:
  and $1, $2, $3
  $1 = $2 & $3
  xori $1, $2, 0xFF12
  $1 = $2 ^ 0x0000FF12
  See all in textbook!

## Slide 23: Summary - 1

## Slide 24: Summary - 2

## Slide 25: MIPS Instruction Decoding Ring
Top table summarizes opcodes
Bottom table summarizes func field if opcode is 000000
OP | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
000 | func |  | j | jal | beq | bne |  | 
001 | addi | addiu | slti | sltiu | andi | ori | xori | lui
010 |  |  |  |  |  |  |  | 
011 |  |  |  |  |  |  |  | 
100 |  |  |  | lw |  |  |  | 
101 |  |  |  | sw |  |  |  | 
110 |  |  |  |  |  |  |  | 
111 |  |  |  |  |  |  |  | 
func | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
000 | sll |  | srl | sra | sllv |  | srlv | srav
001 | jr | jalr |  |  |  |  |  | 
010 |  |  |  |  |  |  |  | 
011 | mult | multu | div | divu |  |  |  | 
100 | add | addu | sub | subu | and | or | xor | nor
101 |  |  | slt | sltu |  |  |  | 
110 |  |  |  |  |  |  |  | 
111 |  |  |  |  |  |  |  | 

## Slide 26: Summary
We will use a subset of MIPS instruction set in this class
  Sometimes called “miniMIPS”
  All instructions are 32-bit
  3 basic instruction formats
    R-type - Mostly 2 source and 1 destination register
    I-type - 1-source, a small (16-bit) constant, and a destination register
    J-type - A large (26-bit) constant used for jumps
  Load/Store architecture
  31 general purpose registers, one hardwired to 0, and, by convention, several are used for specific purposes.
ISA design requires tradeoffs, usually based on
  History, Art, Engineering
  Benchmark results