## Slide 1: Computer Organization and Design Transistors and all that… a brief overview
Montek Singh
Mar 21, 2016
Lecture 9

## Slide 2: Today’s Topics
Where are we in this course?
Today’s topics
  Why go digital?
  Encoding bits using voltages
  Digital design primitives
    transistors and gates

## Slide 3: Let’s go digital!
Why DIGITAL?
  … because it helps guarantee a reliable system
The price we pay for this robustness?
  All the information that we transfer between components is only 1 crummy bit!
  But, in exchange, we get a guarantee of a reliable system.
0 or 1

## Slide 4: The Digital Abstraction
Real World
“Ideal” Abstract World
Volts or
Electrons or
Ergs or Gallons
Bits
0/1
Keep in mind, the world is not digital, we engineer it to behave so. We must use real physical phenomena to implement digital designs!
Noise
Manufacturing Variations

## Slide 5: Types of Digital Components
Two categories of components
  those whose output only depends on their current inputs
    called COMBINATIONAL
    they are “memory-less”, don’t remember the past
  those who output depends also on their past state
    called SEQUENTIAL
    they are “state-holding”, remember their past
    key to building memories

## Slide 6: Terminology
System
  a reasonably large assembly of components
  division of a system into components is typically arbitrary but almost always hierarchical
Component/Element
  an individual part of a bigger system
  clearly-defined function and interface
  implement it and put a black-box around it
  larger components created using smaller components
Circuit
  a small (often leaf-level) component consisting of a network of gates

## Slide 7: Combinational Components
A circuit is combinational if-and-only-if it has:
  one or more digital inputs
  one or more digital outputs
  a functional specification that details the value of each output for every possible combination of valid input values
    output depends only on the latest inputs
  a timing specification consisting (at minimum) of an upper bound tpd on the time this circuit will take to produce the output value once stable valid input values are applied
Output a “1” if at
least 2 out of 3 of
my inputs are a “1”.
Otherwise, output “0”.
I will generate a valid
output in no more than
2 minutes after
seeing valid inputs
input A
input B
input C
output Y

## Slide 8: A Combinational Digital System
Theorem: A system of interconnected elements is combinational if-and-only-if:
  each primitive circuit element is combinational
  every input is connected to exactly one output or directly to a source of 0’s or 1’s
  the circuit contains no directed cycles
    no feedback (yet!)
Proof: By induction
  Start with the rightmost level of elements
    their output only depends on their inputs, which in turn are outputs of the level of element just to their left
    and so on… until you arrive at the leftmost inputs
But, in order to realize digital processing elements we have one more requirement!

## Slide 9: Noise Margins
Key idea: Keep “0”s distinct from the “1”s
  say, “0” is represented by min voltage (e.g., 0 volts)
  … “1” is represented by high voltage (e.g., 1.8 volts)
  use the same voltage representation throughout the entire system!
For reliability, outlaw “close calls”
  forbid a range of voltages between “0” and “1”
volts
Forbidden Zone
Valid
“0”
Valid
“1”
Invalid
CONSEQUENCE: Notion of “VALID” and “INVALID” logic levels
Min Voltage
Max Voltage

## Slide 10: Digital Processing Elements
AND
Some digital processing elements occur so frequently that we give them special names and symbols
A
Y
I will only output a ‘1’ if all my
inputs are ‘1’
A
B
Y
OR
I will output a
‘1’ if any of my
inputs are ‘1’
A
B
Y
A
Y
A
B
Y
XOR
I will only output a
‘1’ if an odd number
of my inputs are ‘1’
buffer
inverter
I will output the complement of
my input
I will copy and restore my input to my output

## Slide 11: Digital Processing Elements
AND
Some digital processing elements occur so frequently that we give them special names and symbols
A
Y
A
B
Y
OR
A
B
Y
A
Y
A
B
Y
XOR
buffer
inverter

## Slide 12: Most common technology today
… is called CMOS
  everything built using transistors
  a transistor is just a switch
2 types of transistors
  n-type
    called “NFET”, or “nMOS” or “n channel transistor” or “n transistor”
    switch is on (i.e., conducts) when its control input is ‘1’
  p-type
    called “PFET”, or “pMOS”, or “p channel transistor” or “p transistor”
    switch is on (i.e., conducts) when its control input is ‘0’
  need both types to build useful gates

## Slide 13: Transistors as switches
At an abstract level, transistors are merely switches
  3-ported voltage-controlled switch
    n-type: conduct when control input is 1
    p-type: conduct when control input is 0

## Slide 14: Silicon as a semiconductor
Transistors are built from silicon
Pure Si itself does not conduct well
Impurities are added to make it conducting
  As provides free electrons  n-type
  B provides free “holes”  p-type
Silicon lattice and dopant atoms (from Harris and Harris)

## Slide 15: MOS Transistors
MOS = Metal-oxide semiconductor
3 terminals
  gate: the voltage here controls whether current flows
  source and drain: are what the current flows between
    structurally, source and drain are the same
nMOS and pMOS transistors (from Harris and Harris)

## Slide 16: nMOS Transistors
Gate = 0
  OFF = disconnect
    no current flows between source & drain
Gate = 1
  ON= connect
    current can flow between source & drain
    positive gate voltage draws in electrons to form a channel
nMOS transistor operation (from Harris and Harris)

## Slide 17: pMOS Transistors
Just the opposite
  Gate = 1  disconnect
  Gate = 0  connect

## Slide 18: Summary: nMOS and pMOS Transistors
Summary:
Notes: N type top
P type bottom
P type has a circle at the gate
Transistor only makes a connection or breaks a connection

## Slide 19: CMOS Topologies
There is actually more to it than connect/disconnect
  nMOS: pass good 0’s, but bad 1’s
    so connect source to GND
  pMOS: pass good 1’s, but bad 0’s
    so connect source to VDD
Typically use them in complementary fashion:
  nMOS network at bottom
    pulls output value down to 0
  pMOS network at top
    pulls output value up to 1
  only one of the two networks must conduct at a time!
    or smoke may be produced
  if neither network conducts  output will be floating
Notes: P transistors always a the top connected to high voltage (t shaped thing rep. overhead high voltage wire)
N is always at the bottom (the triangle indicates ground which is zero voltage)
N can either make or break a path from the ground to the output
Input goes into both, and output comes out
Path could be made from ground to output, which means output gets connected to ground and output is zero.
P is suppose to make a path from 1 to the output, meaning the output becomes 1
N transistors are “pull down network” pulls the output voltage to 0

## Slide 20: From Transistors… to Gates!
Logic Gate recipe:
  use complementary arrangements of PFETs and NFETs
    called CMOS (“complementary metal-oxide semiconductor”)
  at any time: either “pullup” active, or “pulldown”, never both!
VDD
VIN
VOUT
pullup: make this connection when VIN is near 0 so that VOUT = VDD
pulldown: make this connection when VIN is near VDD so that VOUT = 0
We’ll use p-type here
and, n-type here
Gnd
Notes: If the input is 0, the top will conduct and try to send a 1 to the output
If the input is 1, the top is disconnected so the output gets connect to zero and the output is zero

## Slide 21: CMOS Inverter
Vin
Vout
Vin
Vout
A
Y
inverter
Only a narrow range of input voltages result in “invalid” output values. (This diagram is greatly exaggerated)
Valid “1”
Valid “0”
Invalid
“1”
“0”
“0”
“1”
Notes: What if the input is between zero and one?

## Slide 22: CMOS Complements
conducts when A is high
conducts when A is low
conducts when A is high and B is high: A.B
A
B
A
B
conducts when A is low or B is low: A+B = A.B
conducts when A is high or B is high: A+B
A
B
A
B
conducts when A is low and B is low: A.B = A+B
A
A
Series N connections:
Parallel N connections:
Parallel P connections:
Series P connections:

## Slide 23: A Two Input Logic Gate
A
B
What function does
this gate compute?
A B Y
0 0
0 1
1 0
1 1
(see next slide)
Y

## Slide 24: NAND
A | B | P1 | P2 | N1 | N2 | Y
0 | 0 | ON | ON | OFF | OFF | 1
0 | 1 | ON | OFF | OFF | ON | 1
1 | 0 | OFF | ON | ON | OFF | 1
1 | 1 | OFF | OFF | ON | ON | 0

## Slide 25: Here’s Another…
What function does
this gate compute?
A B C
0 0
0 1
1 0
1 1
A
B
2-input NOR gate
1
0
0
0

## Slide 26: 3-input NOR Gate?

## Slide 27: Drawing Style
Indicate inputs and outputs using arrows
  or: inputs at left/top, outputs at right/bottom
If possible, gates should flow from left to right
  or: top to bottom
Straight wires best
  or: keep bends at a minimum (preferably 90 deg)
Connections:
  wires always connect at a “T” junction
  a dot at a wire crossing indicates connection
  wire crossing without a dot means no connection

## Slide 28: Circuit Schematic Rules (cont.)
Wire connections
  A dot where wires cross indicates a connection
  Wires crossing without a dot make no connection
  Wires always connect at a T junction

## Slide 29: CMOS Gates Like to Invert
Observation: CMOS gates tend to be inverting!
  One or more “0” inputs are necessary to generate a “1” output
  One or more “1” inputs are necessary to generate a “0” output
  Why?
A
B

## Slide 30: General CMOS Gate Recipe
Step 1. Figure out pulldown network that does what you want (i.e the set of conditions where the output is ‘0’) e.g., F = A*(B+C)
A
B
C
Step 2. Walk the hierarchy replacing nfets with pfets, series subnets with parallel subnets, and parallel subnets with series subnets
A
B
C
Step 3. Combine pfet pullup network from Step 2 with nfet pulldown
network from Step 1 to form fully-complementary CMOS gate.
A
B
C
A
B
C
Notes: A must be on, either B or C has to be on to work

## Slide 31: One More Exercise
Lets construct a gate to compute:
  F = A+BC = NOT(OR(A,AND(B,C)))
  Step 1: Draw the pull-down network
  Step 2: The complementary pull-up network
F
A
B
C
Vdd
A
B
C

## Slide 32: One More Exercise
Lets construct a gate to compute:
  F = A+BC = NOT(OR(A,AND(B,C)))
  Step 1: Draw the pull-down network
  Step 2: The complementary pull-up network
  Step 3: Combine and Verify
F
A
B
C
Vdd
A
B
C
A | B | C | F
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
1
1
1
0
0
0
0
0