## Slide 1: Computer Organization and Design Arithmetic & Logic Circuits
Montek Singh
Apr 1, 2016
Lecture 11

## Slide 2: Topics
Arithmetic Circuits
  adder
  subtractor
Logic Circuits
Arithmetic & Logic Unit (ALU)
  … putting it all together

## Slide 3: Review: 2’s Complement
8-bit 2’s complement example:
  11010110 = – 128 + 64 + 16 + 4 + 2 = – 42
Beauty of 2’s complement representation:
  same binary addition procedure will work for adding both signed and unsigned numbers
    as long as the leftmost carry out is properly handled/ignored
Insert a “binary” point to represent fractions too:
  1101.0110 = – 8 + 4 + 1 + 0.25 + 0.125 = – 2.625
20
21
22
23
…
2N-2
-2N-1
…
…
N bits
“sign bit”
“binary” point
Range: – 2N-1 to 2N-1 – 1

## Slide 4: Binary Addition
Example of binary addition “by hand”:
Let’s design a circuit to do it!
  Start by building a block that adds one column:
    called a “full adder” (FA)
  Then cascade them to add two numbers of any size…
A: 1101 B:+ 0101 10010
1
0
1
1
Carries from previous column
Adding two N-bit numbers produces an (N+1)-bit result
A B
CO CI
S
FA
A3 B3 A2 B2 A1 B1 A0 B0
S4 S3 S2 S1 S0
A B
CO CI
S
FA
A B
CO CI
S
FA
A B
CO CI
S
FA
A B
CO CI
S
FA
4-bit adder

## Slide 5: Binary Addition
Extend to arbitrary # of bits
  n bits: cascade n full adders
  Called “Ripple-Carry Adder”
    carries ripple through from right to left
    longest chain of carries has length n
      how long does it take to add the numbers 0 and 1?
      how long does it take to add the numbers -1 and 1?
An-1 Bn-1 A2 B2 A1 B1 A0 B0
Sn Sn-1 S2 S1 S0
A B
CO CI
S
FA
A B
CO CI
S
FA
A B
CO CI
S
FA
A B
CO CI
S
FA

## Slide 6: Designing a Full Adder (1-bit adder)
Follow the step-by-step method
  Start with a truth table:
  Write down eqns for the “1” outputs:
  Simplifying a bit (seems hard, but experienced designers are good at this art!)

## Slide 7: For Those Who Prefer Logic Diagrams
A little tricky, but only 5 gates/bit!
Ci
A B
S
Co
“Sum”
Logic
“Carry”
Logic

## Slide 8: Subtraction: A-B = A + (-B)
Subtract B from A = add 2’s complement of B to A
  In 2’s complement: –B = ~B + 1
  Let’s build an arithmetic unit that does both add and sub
    operation selected by control input:
But what about the “+1”?
A B
CO CI
S
FA
A B
CO CI
S
FA
A B
CO CI
S
FA
A B
CO CI
S
FA
A3 A2 A1 A0
S4 S3 S0 S1 S0
B3 B2 B1 B0
Subtract
~ = bit-wise complement
B
0
B
B
1
B

## Slide 9: Condition Codes
One often wants 4 other bits of information from an arith unit:
  Z (zero): result is = 0
    big NOR gate
  N (negative): result is < 0
    SN-1
  C (carry): indicates that most significant position produced a carry, e.g., “1 + (-1)”
    Carry from last FA
  V (overflow): indicates answer doesn’t fit
    precisely:
To compare A and B,
perform A–B and use
condition codes:
Signed comparison:
EQ == Z
NE != ~Z
LT < NV LE <= Z+(NV)
GE >= ~(NV)
GT > ~(Z+(NV))
Unsigned comparison:
EQ == Z
NE != ~Z
LTU < ~C
LEU <= ~C+Z GEU >= C
GTU > ~(~C+Z)
-or-

## Slide 10: Condition Codes
Subtraction is useful also for comparing numbers
To compare A and B:
  First compute A – B
  Then check the flags Z, N, C, V
Examples:
  LTU (less than for unsigned numbers)
    A < B is given by ~C
  LT (less than for signed numbers)
    A < B is given by NV
  Others in table
To compare A and B,
perform A–B and use
condition codes:
Signed comparison:
EQ == Z
NE != ~Z
LT < NV LE <= Z+(NV)
GE >= ~(NV)
GT > ~(Z+(NV))
Unsigned comparison:
EQ == Z
NE != ~Z
LTU < ~C
LEU <= ~C+Z GEU >= C
GTU > ~(~C+Z)

## Slide 11: Latency of Ripple-Carry Adder
Worse-case path: carry propagation from LSB to MSB, e.g., when adding 11…111 to 00…001.
tPD = (tPD,XOR +tPD,AND + tPD,OR) +(N-2)*(tPD,OR + tPD,AND) + tPD,XOR
 (N)
CI to CO
CIN-1 to SN-1
(N) is read “order N” and tells us that the latency of our adder grows in proportion to the number of bits in the operands.
A B
CO CI
S
FA
A B
CO CI
S
FA
A B
CO CI
S
FA
An-1 Bn-1 An-2 Bn-2 A2 B2 A1 B1 A0 B0
Sn-1 Sn-2 S2 S1 S0
A B
CO CI
S
FA
A B
CO CI
S
FA
C
…
CI
A B
S
CO
A,B to CO
(TPD = max propagation delay or latency of the entire adder)

## Slide 12: Can we add faster?
Yes, there are many sophisticated designs that are faster…
  Carry-Lookahead Adders (CLA)
  Carry-Skip Adders
  Carry-Select Adders
   See textbook for details

## Slide 13: Adder Summary
Adding is not only common, but it is also tends to be one of the most time-critical of operations
  As a result, a wide range of adder architectures have been developed that allow a designer to tradeoff complexity (in terms of the number of gates) for performance.
Ripple Carry
Carry
Skip
Carry
Select
Carry
Lookahead
Smaller / Slower
Bigger / Faster
Add
A
B
S
Add/Sub
A
B
S
sub
At this point we’ll define a high-level functional unit for an adder, and specify the details of the implementation as necessary.

## Slide 14: Shifting and Logical Operations

## Slide 15: Shifting Logic
Shifting is useful for logic operations
  applied to groups of bits
  used for alignment
Shifting also used for “short cut” arithmetic operations
  shift left logical (sll)
    X << 1 is the same as 2*X (unless result overflows)
  shift right logical (srl)
    X >> 1 is the same as X/2 for unsigned numbers
  shift right arithmetic (sra)
    like a right shift, but maintains the sign bit
    makes the sign bit “sticky”
    X >>> 1 is the same as X/2 for 2’s-compl. numbers

## Slide 16: Shifting Logic
Examples:
  X = 2010 = 000101002
  Left Shift: shifts in a 0 from the right end
    (X << 1) = 001010002 = 4010
  Right Shift: shifts in a 0 from the left end
    (X >> 1) = 000010102 = 1010
  Signed or “Arithmetic” Right Shift: maintains the sign bit
    -X = -2010 = 2’s complement of X = 111011002
    (-2010 >>> 1) = (111011002 >>> 1) = 111101102 = -1010

## Slide 17: Shifting Logic: Other shift amounts
Circuit for shifting left by 1
  if SLL1 is true
    shifts the input X: R  X << 1
  if SLL1 is false
    does not shift X: R  X
Other shift amounts
  shift left by 2
    rewire the multiplexors so each Xi feeds into Ri+2
  similarly: shift left by 4, etc.
  also: srl and sra have similar circuitry
    srl: each Xi feeds into a lower numbered Rj
    sra: sign bit stays the same
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
R7
R6
R5
R4
R3
R2
R1
R0
X7
X6
X5
X4
X3
X2
X1
X0
“0”
SLL1

## Slide 18: Shifting Logic: Other shift amounts
Circuit for shifting left by any amount
  make blocks for SLL1, SLL2, SLL4, SLL8, SLL16
  then, any arbitrary shift amount can be made by combining these shifts
  example: SLL 13 = SLL (8 + 4 + 1)
shift
left
by 16
SLL16
shift
left
by 8
SLL8
shift
left
by 4
SLL4
shift
left
by 2
SLL2
shift
left
by 1
SLL1
0
1
1
0
1
13 = 01101 in binary!
shift amount

## Slide 19: Boolean Operations
It will also be useful to perform logical operations on groups of bits. Which ones?
  ANDing is useful for “masking” off groups of bits.
    ex. 10101110 & 00001111 = 00001110 (mask selects last 4 bits)
  ANDing is also useful for “clearing” groups of bits.
    ex. 10101110 & 00001111 = 00001110 (0’s clear first 4 bits)
  ORing is useful for “setting” groups of bits.
    ex. 10101110 | 00001111 = 10101111 (1’s set last 4 bits)
  XORing is useful for “complementing” groups of bits.
    ex. 10101110 ^ 00001111 = 10100001 (1’s invert last 4 bits)
  NORing is useful for.. uhm…
    ex. 10101110 # 00001111 = 01010000 (0’s invert, 1’s clear)

## Slide 20: Boolean Unit
It is simple to build up a Boolean unit using primitive gates and a mux to select the function.
  Since there is no interconnection between bits, this unit can be simply replicated at each position.
  The cost is about 7 gates per bit. One for each primitive function, and approx 3 for the 4-input mux.
This is a straightforward, but not too elegant of a design.
Ai
Bi
Qi
Bool
00 01 10 11
This logic block is repeated for each bit (i.e. 32 times)
2

## Slide 21: An ALU, at last (without comparisons)
Combine add/sub, shift and Boolean units
• Bool 2-bit used also for shift flavor
• A shift amount that B is shifted by
Flags N,V,C
A
B
Result
Bidirectional
Shifter
Boolean
Add/Sub
Sub
Bool
Shft
Math
1 0
1 0
Z
Flag
Sub Bool Shft Math OP
0 XX 0 1 A+B
1 XX 0 1 A-B
X 00 1 0 B<<A X 10 1 0 B>>A
X 11 1 0 B>>>A
X 00 0 0 A & B
X 01 0 0 A | B
X 10 0 0 A ^ B
X 11 0 0 A | B
5-bit ALUFN

## Slide 22: A Complete ALU
With support for comparisons (LT and LTU)
  LTU = ~C and LT = NV
Sub Bool Shft Math OP
0 XX 0 1 A+B
1 XX 0 1 A-B
1 X0 1 1 A LT B
1 X1 1 1 A LTU B
X 00 1 0 B<<A X 10 1 0 B>>A
X 11 1 0 B>>>A
X 00 0 0 A & B
X 01 0 0 A | B
X 10 0 0 A ^ B
X 11 0 0 A | B
5-bit ALUFN
A
B
Result
Bidirectional
Shifter
Boolean
Add/Sub
Sub
Bool
Shft
Math
1 0
1 0
Z
Flag
Flags N,V,C
Bool0
0 1
<?

## Slide 23: Next
Circuits for
  Multiplication
  Division
  Floating-Point Operations