## Slide 1: Computer Organization and Design More Arithmetic: Multiplication, Division & Floating-Point
Montek Singh
Apr 8, 2016
Lecture 12

## Slide 2: Topics
Brief overview of:
  integer multiplication
  integer division
  floating-point numbers and operations
Reading: Study Chapter 3.3-3.5

## Slide 3: Binary Multipliers
× | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
2 | 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18
3 | 0 | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27
4 | 0 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36
5 | 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45
6 | 0 | 6 | 12 | 18 | 24 | 30 | 36 | 42 | 48 | 54
7 | 0 | 7 | 14 | 21 | 28 | 35 | 42 | 49 | 56 | 63
8 | 0 | 8 | 16 | 24 | 32 | 40 | 48 | 56 | 64 | 72
9 | 0 | 9 | 18 | 27 | 36 | 45 | 54 | 63 | 72 | 81
× | 0 | 1
0 | 0 | 0
1 | 0 | 1
You’ve got to be kidding… It can’t be that easy!
The key trick of multiplication is memorizing a digit-to-digit table… Everything else is just adding

## Slide 4: Binary Multiplication
A0
A1
A2
A3
B0
B1
B2
B3
A0B0
A1B0
A2B0
A3B0
A0B1
A1B1
A2B1
A3B1
A0B2
A1B2
A2B2
A3B2
A0B3
A1B3
A2B3
A3B3
x
+
AjBi is a “partial product”
Multiplying N-digit number by M-digit number gives (N+M)-digit result
Easy part: forming partial products (just an AND gate since BI is either 0 or 1)
Hard part: adding M, N-bit partial products
1
0
1
0
0
0
1
0
X
The “Binary” Multiplication Table
Hey, that looks like an AND gate
Binary multiplication is implemented using the same basic longhand algorithm that you learned in grade school.

## Slide 5: Multiplication: Implementation
D
o
n
e
1
.
T
e
s
t
M
u
l
t
i
p
l
i
e
r
0
1
a
.
A
d
d
m
u
l
t
i
p
l
i
c
a
n
d
t
o
p
r
o
d
u
c
t
a
n
d
p
l
a
c
e
t
h
e
r
e
s
u
l
t
i
n
P
r
o
d
u
c
t
r
e
g
i
s
t
e
r
2
.
S
h
i
f
t
t
h
e
M
u
l
t
i
p
l
i
c
a
n
d
r
e
g
i
s
t
e
r
l
e
f
t
1
b
i
t
3
.
S
h
i
f
t
t
h
e
M
u
l
t
i
p
l
i
e
r
r
e
g
i
s
t
e
r
r
i
g
h
t
1
b
i
t
3
2
n
d
r
e
p
e
t
i
t
i
o
n
?
S
t
a
r
t
M
u
l
t
i
p
l
i
e
r
0
=
0
M
u
l
t
i
p
l
i
e
r
0
=
1
N
o
:
<
3
2
r
e
p
e
t
i
t
i
o
n
s
Y
e
s
:
3
2
r
e
p
e
t
i
t
i
o
n
s
Flow Chart
Hardware
Implementation

## Slide 6: Second Version
M
u
l
t
i
p
l
i
e
r
S
h
i
f
t
r
i
g
h
t
W
r
i
t
e
3
2
b
i
t
s
6
4
b
i
t
s
3
2
b
i
t
s
S
h
i
f
t
r
i
g
h
t
M
u
l
t
i
p
l
i
c
a
n
d
3
2
-
b
i
t
A
L
U
P
r
o
d
u
c
t
C
o
n
t
r
o
l
t
e
s
t
D
o
n
e
1
.
T
e
s
t
M
u
l
t
i
p
l
i
e
r
0
1
a
.
A
d
d
m
u
l
t
i
p
l
i
c
a
n
d
t
o
t
h
e
l
e
f
t
h
a
l
f
o
f
t
h
e
p
r
o
d
u
c
t
a
n
d
p
l
a
c
e
t
h
e
r
e
s
u
l
t
i
n
t
h
e
l
e
f
t
h
a
l
f
o
f
t
h
e
P
r
o
d
u
c
t
r
e
g
i
s
t
e
r
2
.
S
h
i
f
t
t
h
e
P
r
o
d
u
c
t
r
e
g
i
s
t
e
r
r
i
g
h
t
1
b
i
t
3
.
S
h
i
f
t
t
h
e
M
u
l
t
i
p
l
i
e
r
r
e
g
i
s
t
e
r
r
i
g
h
t
1
b
i
t
3
2
n
d
r
e
p
e
t
i
t
i
o
n
?
S
t
a
r
t
M
u
l
t
i
p
l
i
e
r
0
=
0
M
u
l
t
i
p
l
i
e
r
0
=
1
N
o
:
<
3
2
r
e
p
e
t
i
t
i
o
n
s
Y
e
s
:
3
2
r
e
p
e
t
i
t
i
o
n
s
More Efficient Hardware
Implementation
Flow Chart

## Slide 7: Final Version
D
o
n
e
1
.
T
e
s
t
P
r
o
d
u
c
t
0
1
a
.
A
d
d
m
u
l
t
i
p
l
i
c
a
n
d
t
o
t
h
e
l
e
f
t
h
a
l
f
o
f
t
h
e
p
r
o
d
u
c
t
a
n
d
p
l
a
c
e
t
h
e
r
e
s
u
l
t
i
n
t
h
e
l
e
f
t
h
a
l
f
o
f
t
h
e
P
r
o
d
u
c
t
r
e
g
i
s
t
e
r
2
.
S
h
i
f
t
t
h
e
P
r
o
d
u
c
t
r
e
g
i
s
t
e
r
r
i
g
h
t
1
b
i
t
3
2
n
d
r
e
p
e
t
i
t
i
o
n
?
S
t
a
r
t
P
r
o
d
u
c
t
0
=
0
P
r
o
d
u
c
t
0
=
1
N
o
:
<
3
2
r
e
p
e
t
i
t
i
o
n
s
Y
e
s
:
3
2
r
e
p
e
t
i
t
i
o
n
s
The trick is to use the lower half of the product to hold the multiplier during the operation.
Even More Efficient
Hardware Implementation!

## Slide 8: Example for second version
0010 1100 0001 0110
0010
0001 0000
Test true shift right
4
0001 1000 0000 1100
0010
0010 0001
Test false shift right
3
0011 0000 0001 1000
0010
0101 0010
Test true shift right
2
0010 0000 0001 0000
0010
1011 0101
Test true shift right
1
0000 0000
0010
1011
Initial
0
Product
Multiplicand
Multiplier
Step
Iteration

## Slide 9: What about the sign?
Positive numbers are easy
How about negative numbers?
  Please read signed multiplication in textbook (Ch 3.3)

## Slide 10: Can do we faster?
Instead of iterating in time…
How about iterating in space…?
  repeat circuits in space
    consume more area
    but faster computation

## Slide 11: Simple Combinational Multiplier
“Array Multiplier”
  repetition in space, instead of time
  Components used:
    N*(N-1) full adders
    N2 AND gates

## Slide 12: Simple Combinational Multiplier
Propagation delay
  Proportional to N
    N is #bits in each operand
  ~ 3N*tpd,FA

## Slide 13: Division
Flow Chart
Hardware
Implementation
See example in textbook (Fig 3.10)

## Slide 14: Floating-Point Numbers & Arithmetic
Reading: Study Chapter 3.5

## Slide 15: Why do we need floating point?
Several reasons:
  Many numeric applications need numbers over a huge range
    e.g., nanoseconds to centuries
  Most scientific applications require real numbers (e.g. )
But so far we only have integers. What do we do?
  We could implement the fractions explicitly
    e.g.: ½, 1023/102934
  We could use bigger integers
    e.g.: 64-bit integers
  Floating-point representation is often better
    has some drawbacks too!

## Slide 16: Recall Scientific Notation
Recall scientific notation from high school
  Numbers represented in parts:
    42 = 4.200 x 101
    1024 = 1.024 x 103
    -0.0625 = -6.250 x 10-2
Arithmetic is done in pieces
  1024 1.024 x 103
  - 42 -0.042 x 103
  = 982 0.982 x 103
  = 9.820 x 102
Before adding, we must match the exponents, effectively “denormalizing” the smaller magnitude number
We then “normalize” the final result so there is one digit to the left of the decimal point and adjust the exponent accordingly.
Significant Digits
Exponent

## Slide 17: Multiplication in Scientific Notation
Is straightforward:
  Multiply together the significant parts
  Add the exponents
  Normalize if required
Examples:
  1024 1.024 x 103
  x 0.0625 6.250 x 10-2
  = 64 6.400 x 101
  42 4.200 x 101
  x 0.0625 6.250 x 10-2
  = 2.625 26.250 x 10-1
  = 2.625 x 100 (Normalized)
In multiplication, how far is the most you will ever normalize?
In addition?

## Slide 18: Binary Floating-Point Notation
IEEE single precision floating-point format
  Example: (0x42280000 in hexadecimal)
Three fields:
  Sign bit (S)
  Exponent (E): Unsigned “Bias 127” 8-bit integer
    E = Exponent + 127
    Exponent = 10000100 (132) – 127 = 5
  Significand (F): Unsigned fixed-point with “hidden 1”
    Significand = “1”+ 0.01010000000000000000000 = 1.3125
  Final value: N = -1S (1+F) x 2E-127 = -10(1.3125) x 25 = 42
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0
“F” Significand (Mantissa) - 1
“E”
Exponent + 127
“S”
Sign Bit
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Notes: In floating point, two’s complement does not work because things aren’t aligned correctly. This is because of the exponents…
You need a leftmost sign bit which indicates either negative or positive, if it is 0 it is positive
The green E is the expononent, the exponent also allows negatives using a bias. All numbers get 127 added to it, so if you want 0 you make it 127
Significand is a decimal with an added assumed 1

## Slide 19: Example Numbers
One
  Sign = +, Exponent = 0, Significand = 1.0
    1 = -10 (1.0) x 20
    S = 0, E = 0 + 127, F = 1.0 – ‘1’
    0 01111111 00000000000000000000000 = 0x3f800000
One-half
  Sign = +, Exponent = -1, Significand = 1.0
    ½ = -10 (1.0) x 2-1
    S = 0, E = -1 + 127, F = 1.0 – ‘1’
    0 01111110 00000000000000000000000 = 0x3f000000
Minus Two
  Sign = -, Exponent = 1, Significand = 1.0
    -2 = -11 (1.0) x 21
    1 10000000 00000000000000000000000 = 0xc0000000
Notes: Number one:
sign is positive so s = 0
exponent is 0, after a bias of 127 the E field is 127 whch is 01111111
The fraction is 1.0, but you only store after the point so it is all 0’s
One half:
Minus two:
the sign bit is negative so it is 1

## Slide 20: Zeros
How do you represent 0?
  Sign = ?, Exponent = ?, Significand = ?
    Here’s where the hidden “1” comes back to bite you
    Hint: Zero is small. What’s the smallest number you can generate?
      Exponent = -127, Signficand = 1.0
      -10 (1.0) x 2-127 = 5.87747 x 10-39
IEEE Convention
  When E = 0 (Exponent = -127), we’ll interpret numbers differently…
    0 00000000 00000000000000000000000 = 0 not 1.0 x 2-127
    1 00000000 00000000000000000000000 = -0 not -1.0 x 2-127
Yes, there are “2” zeros. Setting E=0 is also used to represent a few other small numbers besides 0. In all of these numbers there is no “hidden” one assumed in F, and they are called the “unnormalized numbers”. WARNING: If you rely these values you are skating on thin ice!
Notes: In the special case, when the exponent of 2 is -127, you say that there is no hidden one before the dot, it is a hidden zero.
When there exponent is -127 it is a zero

## Slide 21: Infinities
IEEE floating point also reserves the largest possible exponent to represent “unrepresentable” large numbers
  Positive Infinity: S = 0, E = 255, F = 0
    0 11111111 00000000000000000000000 = +∞
    0x7f800000
  Negative Infinity: S = 1, E = 255, F = 0
    1 11111111 00000000000000000000000 = -∞
    0xff800000
  Other numbers with E = 255 (F ≠ 0) are used to represent exceptions or Not-A-Number (NAN)
    √-1, -∞ x 42, 0/0, ∞/∞, log(-5)
  It does, however, attempt to handle a few special cases:
    1/0 = + ∞, -1/0 = - ∞, log(0) = - ∞
Notes: If the E field is all 1’s and the fraction field is all 0’s it is a special pattern that indicates infinity. The sign field denotes positive vs. negative
The E field being all 1’s and the fraction field being not all 0’s are special numbers

## Slide 22: Low-End of the IEEE Spectrum
denorm
gap
“Denormalized Gap”
  The gap between 0 and the next representable normalized number is much larger than the gaps between nearby representable numbers
  IEEE standard uses denormalized numbers to fill in the gap, making the distances between numbers near 0 more alike
    Denormalized numbers have a hidden “0” and…
    … a fixed exponent of -126
    X = -1S 2-126 (0.F)
      Zero is represented using 0 for the exponent and 0 for the mantissa. Either, +0 or -0 can be represented, based on the sign bit.
0
2-bias
21-bias
22-bias
normal numbers with hidden bit

## Slide 23: Floating point AIN’T NATURAL
It is CRUCIAL for computer scientists to know that Floating Point arithmetic is NOT the arithmetic you learned since childhood
1.0 is NOT EQUAL to 10*0.1 (Why?)
  1.0 * 10.0 == 10.0
  0.1 * 10.0 != 1.0
  0.1 decimal == 1/16 + 1/32 + 1/256 + 1/512 + 1/4096 + … ==
    0.0 0011 0011 0011 0011 0011 …
  In decimal 1/3 is a repeating fraction 0.333333…
  If you quit at some fixed number of digits, then 3 * 1/3 != 1
Floating Point arithmetic IS NOT associative
  x + (y + z) is not necessarily equal to (x + y) + z
Addition may not even result in a change
  (x + 1) MAY == x
Notes: Adding numbers in different orders may not be the same because there could be drops with the vast amounts of nums

## Slide 24: Floating Point Disasters
Scud Missiles get through, 28 die
  In 1991, during the 1st Gulf War, a Patriot missile defense system let a Scud get through, hit a barracks, and kill 28 people. The problem was due to a floating-point error when taking the difference of a converted & scaled integer. (Source: Robert Skeel, "Round-off error cripples Patriot Missile", SIAM News, July 1992.)
$7B Rocket crashes (Ariane 5)
  When the first ESA Ariane 5 was launched on June 4, 1996, it lasted only 39 seconds, then the rocket veered off course and self-destructed. An inertial system, produced a floating-point exception while trying to convert a 64-bit floating-point number to an integer. Ironically, the same code was used in the Ariane 4, but the larger values were never generated (http://www.around.com/ariane.html).
Intel Ships and Denies Bugs
  In 1994, Intel shipped its first Pentium processors with a floating-point divide bug. The bug was due to bad look-up tables used to speed up quotient calculations. After months of denials, Intel adopted a no-questions replacement policy, costing $300M. (http://www.intel.com/support/processors/pentium/fdiv/)

## Slide 25: Optional material
(for self-study only; won’t be tested on)

## Slide 26: Floating-Point Multiplication
S
E
F
S
E
F
× 24 by 24
round
Small ADDER
Mux (Shift Right by 1)
Control
Subtract 127
Add 1
S
E
F
Step 1:
Multiply significands
Add exponents
ER = E1 + E2 -127
(do not need twice the bias)
Step 2:
Normalize result
(Result of [1,2) *[1.2) = [1,4)
at most we shift right one bit, and fix exponent

## Slide 27: Floating-Point Addition

## Slide 28: MIPS Floating Point
Floating point “Co-processor”
  Separate co-processor for supporting floating-point
    Separate circuitry for arithmetic, logic operations
Registers
  F0…F31: each 32 bits
    Good for single-precision (floats)
  Or, pair them up: F0|F1 pair, F2|F3 pair … F30|F31 pair
    Simply refer to them as F0, F2, F4, etc. Pairing implicit from instruction used
    Good for 64-bit double-precision (doubles)

## Slide 29: MIPS Floating Point
Instructions determine single/double precision
  add.s $F2, $F4, $F6 // F2=F4+F6 single-precision add
  add.d $F2, $F4, $F6 // F2=F4+F6 double-precision add
    Really using F2|F3 pair, F4|F5 pair, F6|F7 pair
Instructions available:
  add.d fd, fs, ft # fd = fs + ft in double precision
  add.s fd, fs, ft # fd = fs + ft in single precision
  sub.d, sub.s, mul.d, mul.s, div.d, div.s, abs.d, abs.s
  l.d fd, address # load a double from address
  l.s, s.d, s.s
  Conversion instructions: cvt.w.s, cvt.s.d, …
  Compare instructions: c.lt.s, c.lt.d, …
  Branch (bc1t, bc1f): branch on comparison true/false

## Slide 30: End of optional material

## Slide 31: Next
Sequential circuits
  Those with memory
  Useful for registers, state machines
Let’s put it all together
  … and build a CPU