## Slide 1: Computer Organization and Design Memories and State Machines
Montek Singh
Apr 11-13, 2016
Lecture 13

## Slide 2: Topics
Memory Arrays
Transparent Latches
Edge-triggered Registers
Finite State Machines

## Slide 3: Memory as a Lookup Table
A multiplexer to implement a lookup table:
  Remember that, in theory, we can build any 1-output combinational logic block with multiplexers
  For an N-input function we need a 2N input multiplexer
BIG Multiplexers?
  How about 10-input function? 20-input?
MUX
Logic
A
B
Fn(A,B)
Notes: For N-input function, need
  N select inputs to MUX
  2**N data inputs to MUX (LOTSA pins!)
Practical TABLE LOOKUP needs more efficient
use of space...
2n
2n
2
1024-input MUX???

## Slide 4: A Mux’s Guts
Hmmm, by sharing the decoder part of the logic MUXs could be adapted to make lookup tables with any number of outputs
I
0
0
I
0
1
I
1
0
I
1
1
A
B
A
B
A
B
A
B
Y
Decoder
Selector
Multiplexers can be partitioned into two sections.
A DECODER that identifies the desired input,and
a SELECTOR that enables that input onto the output.
A decoder generates all possible product terms for a set of inputs
0
1
2
3
Notes: ... THIS one AIN’T!
One of the four outputs is true

## Slide 5: A New Combinational Device
k
D1
D2
DN
DECODER:
  k SELECT inputs,
  N = 2k DATA OUTPUTs.
Selected Dj HIGH; all others LOW.
NOW, we are well on our way to building a general purpose table-lookup device.
We can build a 2-dimensional ARRAY of decoders and selectors as follows ...
Notes: DECODER -- sorta inverse MUX.
  BINARY number as input
  UNARY (decoded) output.

## Slide 6: Shared Decoding Logic
We can build a general purpose “table-lookup” device called a Read-Only Memory (ROM), from which we can implement any truth table and, thus, any combinational device

## Slide 7: Logic According to ROMs
ROMs ignore the structure of combinational functions ...
  Size, layout, and design are independent of function
  Any Truth table can be “programmed” by minor reconfiguration:
    Metal layer (masked ROMs)
    Fuses (Field-programmable PROMs)
    Charge on floating gates (EPROMs)
    ... etc.
Model: LOOK UP value of function in truth table...
  Inputs: “ADDRESS” of a truth table entry
  ROM SIZE = # truth table entries...
    ... for an N-input boolean function, size = __________
2N x #outputs
Notes: 2-D: 2x/dimension
NOT OPTIMAL -- Optimized for WORST case
(NO structure in TT entries!)
ADVANTAGE: Flexibility.
CHANGE function with little change in HW.

## Slide 8: Analog Storage: Using Capacitors
We’ve chosen to encode information using voltages and we know from physics that we can “store” a voltage as “charge” on a capacitor
  Pros:
    compact!
  Cons:
    it leaks!  refresh
    complex interface
    reading a bit, destroys it
      (you have to rewrite the value after each read)
    it’s NOT a digital circuit
bit line
N-channel
FET serves
as an access switch
VREF
To write:
Drive bit line, turn on access fet, force storage cap to new voltage To read: precharge bit line, turn on access fet,
detect (small) change in bit line voltage
word
line
This storage circuit is the basis for commodity DRAMs

## Slide 9: A “Digital” Storage Element
Y
S
B
It’s also easy to build a DIGITAL storage element (called a latch) using a MUX and FEEDBACK:
0
1
G
0
0
1
1
D
--
--
0
1
QIN
0
1
--
--
QOUT
0
1
0
1
Q follows D
Q stable
“state” signal
appears as both
input and output
A
D
G
Q
Here’s a feedback path, so it’s no longer a combinational circuit.

## Slide 10: Looking Under the Covers
Let’s take a quick look at the equivalent circuit for our MUX when the control is LOW (the feedback path is active)
D
G=0
Q
Q
G=0
D
0
1
1
1
Q
This storage circuit is the basis for commodity SRAMs
Advantages: 1) Maintains remembered state for as long as power is applied. 2) State is DIGITAL
Disadvantage:
1) Requires more transistors

## Slide 11: Why Does Feedback = Storage?
Key Idea: use positive feedback to maintain storage indefinitely
  logic gates are built to restore marginal signal levels, so noise shouldn’t be a problem!
VIN
VOUT
Result: a “bi-stable” storage element

## Slide 12: Static D Latch
G
D
Q
D
G
Q stable
Q follows D
Positive latch
Q
“static” means latch will hold data (i.e., value of Q) while G is inactive, however long that may be.
G
D
Q
Negative latch
Q
G
D
1
0

## Slide 13: Latch Timing
Circuits with memory must follow some rules
  Guarantee that inputs to sequential devices are valid and stable during periods when they may influence state changes
    This is assured with additional timing specifications
G
D
>tPULSE
tPULSE (minimum pulse width): guarantee G is active for long enough for latch to capture data
>tSETUP
tSETUP (setup time): guarantee that D value has propagated through feedback path before latch becomes opaque
>tHOLD
tHOLD (hold time): guarantee latch is opaque and Q is stable before allowing D to change again
Notes: Data should not be changing while the latch is closing, timing matters
Think of it as a long hallway, do not want data to leak or touch

## Slide 14: Flakey Control Systems
Here’s a strategy for saving 2 bucks the next time you find yourself at a toll booth!
Notes: “having a door to pace the movement of data through a system is not enough”

## Slide 15: Flakey Control Systems
Here’s a strategy for saving 2 bucks the next time you find yourself at a toll booth!

## Slide 16: Flakey Control Systems
WARNING:
Professional Drivers Used!
DON’T try this
At home!
Here’s a strategy for saving 2 bucks the next time you find yourself at a toll booth!

## Slide 17: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 18: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 19: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 20: Escapement Strategy
The Solution:
Add two gates and only open one at a time.
(Psst… Don’t tell the toll folks)

## Slide 21: Escapement Strategy
The Solution:
Add two gates and only open one at a time.
(Psst… Don’t tell the toll folks)

## Slide 22: Escapement Strategy
The Solution:
Add two gates and only open one at a time.
(Psst… Don’t tell the toll folks)

## Slide 23: Escapement Strategy
The Solution:
Add two gates and only open one at a time.
(Psst… Don’t tell the toll folks)

## Slide 24: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 25: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 26: Escapement Strategy
The Solution:
Add two gates and only open one at a time.
(Psst… Don’t tell the toll folks)

## Slide 27: Escapement Strategy
The Solution:
Add two gates and only open one at a time.
(Psst… Don’t tell the toll folks)

## Slide 28: Escapement Strategy
The Solution:
Add two gates and only open one at a time.
(Psst… Don’t tell the toll folks)

## Slide 29: Escapement Strategy
The Solution:
Add two gates and only open one at a time.
(Psst… Don’t tell the toll folks)

## Slide 30: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 31: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 32: Escapement Strategy
The Solution:
Add two gates and only open one at a time.
(Psst… Don’t tell the toll folks)
Key Idea: At no time is there an open path through both gates…

## Slide 33: Edge-triggered Flip Flop
G
D
Q
G
D
Q
Logical “escapement”:
  Double-gated toll booth built using logic gates
Observations:
  only one latch “transparent” at any time:
    master closed when slave is open (CLK is high)
    slave closed when master is open (CLK is low)
    no combinational path all the way through flip flop
  Q only changes shortly after 0 1 transition of CLK, so flip flop appears to be “triggered” by rising edge of CLK
D
Q
D
CLK
Q
D
CLK
Q
master
slave
Transitions mark instants, not intervals
Notes: Use two latches, operating in a complementary fashion
The only different between a flip flop and a latch is the flip flop has a triangle shaped thing

## Slide 34: Flip Flop Waveforms
G
D
Q
G
D
Q
D
Q
D
CLK
Q
D
CLK
Q
master
slave
D
CLK
Q
master closed
slave open
slave closed
master open
Notes: D is data, clk
When the clock is zero, the first latch allows things to come through whatever goes to D goes to the star, the star is frozen during this time
Whenever the clock is one the output follows the star
Each time the clock goes from 0 to 1, internally the two latches are changing
When the clock goes form 0 to 1 the first time D is 1, the output Q is therefore a one
Next time when clock goes form 0 to 1 the value of D is zero and the output Q is 0

## Slide 35: Flip Flop Timing
CLK
D
Q
D
Q
D
CLK
Q
<tPD
tPD: maximum propagation delay, CLK Q
>tSETUP
tSETUP: setup time
  guarantee that D has propagated through feedback path before master closes
>tHOLD
tHOLD: hold time
  guarantee master is closed and data is stable before allowing D to change

## Slide 36: Synchronous Systems
Designing digital systems using a clock

## Slide 37: Synchronous Systems
Flipflop
Combinational
logic
Flipflop
leading
edge
trailing
edge
On the leading edge of the clock, the input of a flipflop is transferred to the output and held.
We must be sure the output of the combinational logic has settled before the next leading clock edge.
Clock
data
Clock period must be “long enough”
Clock Period >= tFF + tlogic + tsetup

## Slide 38: Finite State Machines
What is a State Machine?
  Remember automata?
  It is defined by the following:
    Set of STATES
    Set of INPUTS
    Set of OUTPUTS
    A mapping from (STATES, INPUTS) to …
    … the next STATE and an OUTPUT
  STATE represents memory!

## Slide 39: Implementing an FSM
Use flipflops to represent state (i.e., memory)
Use combinational logic to compute:
  output as a function of inputs + state
  next state as a function of inputs + state
State (flipflops)
Function
(comb. logic)
Inputs
Outputs
Clock
Notes: Flip flops represent states
Could use two flip flops to represent four different states in here

## Slide 40: Example: Traffic Light Controller
4 states
  each corresponding to a circle
  represent states using 2 bits
    00, 01, 10, 11
4 bits of output
  2 bits for east/west light
  2 bits for north/south light
    Red (00)
    Yellow (01)
    Green (10)
G E/W
R N/S
Y E/W
R N/S
R E/W
G N/S
R E/W
Y N/S
Notes: Each side has a light pattern
This state machine could have a late based on being E/W or N/S
When times runs our you change colors
Goes Green yellow red and red green yellow
You have 4 states so need two bits

## Slide 41: Example: Traffic Light Controller
4 states
    00, 01, 10, 11
    need 2 flipflops to represent state
4 bits of output
    R (00), Y (01), G (10)
Truth table:
    this defines the combinational logic part of the FSM
G E/W
R N/S
Y E/W
R N/S
R E/W
G N/S
R E/W
Y N/S
Input (State) | Output | Next State
00 | 10 00 | 01
01 | 01 00 | 10
10 | 00 10 | 11
11 | 00 01 | 00

## Slide 42: Summary
Regular Arrays can be used to implement arbitrary logic functions
Memories
  ROMs are HARDWIRED memories
  RAMs include storage elements that are read-write
    dynamic memory: compact, only reliable short-term
    static memory: controlled use of positive feedback
For static storage:
  Level-sensitive D-latches; edge-triggered flipflops
  Timing issues: setup and hold times
Finite State Machines:
  Implement using flipflops for memory, and combinational logic to compute output, next state