## Slide 1: Computer Organization and Design Pipelining
Montek Singh
Apr 25, 2016
Lecture 16 (Covered very superficially on the final exam)

## Slide 2: Pipelining
Between 411 problems sets, I haven’t had a minute to do laundry
Now that’s what I call dirty laundry

## Slide 3: Laundry Example
Device: Washer
Function: Fill, Agitate, Spin
WasherPD = 30 mins
Device: Dryer
Function: Heat, Spin
DryerPD = 60 mins
INPUT:
dirty laundry
OUTPUT:
4 more weeks

## Slide 4: Laundry: One Load at a Time
Everyone knows that the real reason one puts off doing laundry so long is not because we procrastinate, are lazy, or even have better things to do.
  The fact is, doing laundry one load at a time is not smart.
Step 1:
Step 2:
Total = WasherPD + DryerPD
= _________ mins
90

## Slide 5: Laundry: Doing N Loads!
Here’s how one would do laundry the “unpipelined” way.
Step 1:
Step 2:
Step 3:
Step 4:
Total = N*(WasherPD + DryerPD)
= ____________ mins
N*90
…

## Slide 6: Laundry: Doing N Loads!
Here’s how to “pipeline” the laundry process.
  Much more efficient!
Step 1:
Step 2:
Step 3:
Total = N * Max(WasherPD, DryerPD)
= ____________ mins
N*60
…
Actually, it’s more like N*60 + 30 if we account for the startup time (i.e., filling up the pipeline) correctly. When doing pipeline analysis, we’re mostly interested in the “steady state” where we assume we have an infinite supply of inputs.

## Slide 7: Recall Our Performance Measures
Latency:
  Delay from input to corresponding output
    Unpipelined Laundry = _________ mins
    Pipelined Laundry = _________ mins
Throughput:
  Rate at which inputs or outputs are processed
    Unpipelined Laundry = _________ outputs/min
    Pipelined Laundry = _________ outputs/min
90
120
1/90
1/60
Assuming that the wash is started as soon as possible and waits (wet) in the washer until dryer is available.
Even though
we increase
latency, it takes less time per load

## Slide 8: Pipelining Summary
Advantages:
  Higher throughput than combinational system
  Different parts of the logic work on different parts of the problem…
Disadvantages:
  Generally, increases latency
  Only as good as the *weakest* link (often called the pipeline’s BOTTLENECK)

## Slide 9: Review of CPU Performance
MIPS = Millions of Instr/Second
Freq = Clock Frequency, MHz
CPI = Clocks per Instruction
MIPS =
Freq
CPI
To Increase MIPS:
  1. DECREASE CPI.
    - RISC simplicity reduces CPI to 1.0.
    - CPI below 1.0? State-of-the-art multiple instruction issue
  2. INCREASE Freq.
    - Freq limited by delay along longest combinational path; hence
    - PIPELINING is the key to improving performance.

## Slide 10: Where Are the Bottlenecks?
Pipelining goal:
  Break LONG combinational paths
   memories, ALU in separate stages
WA
PC
+4
Instruction
Memory
A
D
Register
File
RA1
RA2
RD1
RD2
ALU
A
B
WA
ALUFN
Control Logic
Data Memory
RD
WD
R/W
Adr
Wr
WDSEL
0 1 2
BSEL
WDSEL
ALUFN
Wr
J:<25:0>
PCSEL
WERF
WERF
00
PC+4
Rt: <20:16>
Imm: <15:0>
ASEL
SEXT
+
x4
BT
Z
BT
WASEL
Rd:<15:11>
Rt:<20:16>
0
1
2
3
WASEL
PC<31:29>:J<25:0>:00
JT
JT
N
V
C
Z
V
N
C
Rs: <25:21>
ASEL
2
0
SEXT
BSEL
0
1
SEXT
shamt:<10:6>
PCSEL
0
1
2
3
4
5
6
“16”
IRQ
0x80000080
0x80000040
0x80000000
RESET
31
27
1
WD
WE

## Slide 11: Goal: 5-Stage Pipeline
GOAL: Maintain (nearly) 1.0 CPI, but increase clock speed to barely include slowest components (mems, regfile, ALU)
APPROACH: structure processor as 5-stage pipeline:
IF
Instruction Fetch stage: Maintains PC, fetches one instruction per cycle and passes it to
WB
Write-Back stage: writes result back into register file.
ID/RF
Instruction Decode/Register File stage: Decode control lines and select source operands
ALU
ALU stage: Performs specified operation, passes result to …
MEM
Memory stage: If it’s a lw, use ALU result as an address, pass mem data (or ALU result if not lw) to …

## Slide 12: 5-Stage miniMIPS
ALU
A
B
ALUFN
Data Memory
RD
WD
R/W
Adr
Wr
WDSEL
0 1 2
PC+4
Z
V
N
C
PC
+4
Instruction
Memory
A
D
00
BT
PC<31:29>:J<25:0>:00
JT
PCSEL
0
1
2
3
4
5
6
0x80000080
0x80000040
0x80000000
PCREG
00
IRREG
WA
Register
File
RA1
RA2
RD1
RD2
J:<25:0>
Imm: <15:0>
+
x4
BT
JT
Rt: <20:16>
Rs: <25:21>
ASEL
2
0
BSEL
0
1
SEXT
SEXT
shamt:<10:6>
“16”
1
=
BZ
PCALU
00
IRALU
A
B
WDALU
PCMEM
00
IRMEM
YMEM
WDMEM
WA
Register
File
WA
WD
WE
WERF
WASEL
Rd:<15:11>
Rt:<20:16>
“31”
“27”
0 1 2 3
Instruction
Fetch
Register
File
ALU
Write
Back
PCWB
00
IRWB
YWB
Memory
Address is available right after instruction enters Memory stage
Data is needed just before rising clock edge at end of Write Back stage
• Omits some details

## Slide 13: Pipelining
Improve performance by increasing instruction throughput
 Ideal speedup is number of stages in the pipeline. Do we achieve this?

## Slide 14: Pipelining
What makes it easy
  all instructions are the same length
  just a few instruction formats
  memory operands appear only in loads and stores
What makes it hard?
  structural hazards: suppose we had only one memory
  control hazards: need to worry about branch instructions
  data hazards: an instruction depends on a previous instruction
Net effect:
  Individual instructions still take the same number of cycles
  But improved throughput by increasing the number of simultaneously executing instructions

## Slide 15: Data Hazards
Problem with starting next instruction before first is finished
  dependencies that “go backward in time” are data hazards

## Slide 16: Software Solution
Have compiler guarantee no hazards
  Where do we insert the “nops” ?
    Between “producing” and “consuming” instructions! sub $2, $1, $3 and $12, $2, $5 or $13, $6, $2 add $14, $2, $2 sw $15, 100($2)
Problem: this really slows us down!

## Slide 17: Forwarding
Bypass/forward results as soon as they are produced/needed. Don’t wait for them to be written back into registers!

## Slide 18: Can't always forward
Load word can still cause a hazard:
  an instruction tries to read a register following a load instruction that writes to the same register. STALL!

## Slide 19: Stalling
When needed, stall the pipeline by keeping an instruction in the same stage fpr an extra clock cycle.

## Slide 20: Branch Hazards
When branching, other instructions are in the pipeline!
  need to add hardware for flushing instructions if we are wrong

## Slide 21: Pipeline Summary
A very common technique to improve throughput of any circuit
  used in all modern processors!
Fallacies:
  “Pipelining is easy.” No, smart people get it wrong all of the time!
  “Pipelining is independent of ISA.” No, many ISA decisions impact how easy/costly it is to implement pipelining (i.e. branch semantics, addressing modes).
  “Increasing pipeline stages improves performance.” No, returns diminish because of increasing complexity.